WIELAND-DAVCO CORPORATION

CRITICAL LIFT PERMIT

| Section 1: Approvals and Documentation |
| --- |
| A. | Identification |  |  |  |
|  | Subcontract Number: |  | Location: |  |
|  | Lift Identification Name: |  |
|  | Date of Lift: |  | Time: |  |
|  | Lift Description: |  |
| B. | Approvals (Signature Required) |  |  |
|  | Subcontractor: |  | Date: |  |
|  | Subcontractor Lift Supervisor: |  | Date |  |
|  | (This individual must be present during the lift) |  |  |
|  | Project Manager: |  | Date: |  |
|  | WDC Superintendent: |  | Date: |  |
|  | Operator: |  | Date: |  |
|  | Engineering: |  | Date |  |
|  | (If Engineering Designs are used) |  |  |
|  | WDC Safety Rep.: |  | Date: |  |
| C. | Attachments |  |  |
|  |  | 1. | Operator Certifications |  |
|  |  | 2. | Capacity Certificates and Inspection Reports for all Lifting Equipment |
|  |  | 3. | Inspection Reports for all Rigging Equipment |
|  |  | 4. | Rigging Diagram |
|  |  | 5. | Free Body Diagram |

Section 2 :  Pre-Lift Planning

| A. | Pre-Lift Checklist |  |  |  |
| --- | --- | --- | --- | --- |
|  |  | (Initials) |
|  |  | Yes |  | No |
| 1. | Has an inventory of equipment been done? |  |  |  |
| 2. | Have weather conditions been considered? |  |  |  |
| 3. | Have the general safety precautions been reviewed? |  |  |  |
| 4. | Have the electrical safety procedures been reviewed? |  |  |  |
| 5. | Have the safe rigging practices been implemented? |  |  |  |
| 6. | Have the safety precautions been reviewed? |  |  |  |
| 7. | Has a method of attachment and handling been determined? |  |  |  |
| 8. | Are all lifting lugs engineered to specifications? |  |  |  |
| 9. | Has the matting been inspected and approved? |  |  |  |
| 10. | Has the stability of the ground been assured? |  |  |  |
| 11. | Is a tag line going to be used? |  |  |  |
| 12. | Have disconnecting/connecting means been developed? |  |  |  |
| 13. | Has the orientation of equipment been confirmed? |  |  |  |
| 14. | Is survey equipment required? |  |  |  |
| 15. | Is a Pre-Lift Meeting planned? |  |  |  |
| 16. | Is a total weight below 75% of capacity? |  |  |  |
| 17. | Are all required approvals signed? |  |  |  |

Section 3:  Load and Capacity Calculations

| A. | Weight of Equipment – Live Load |  |
| --- | --- | --- |
|  | 1. | Equipment Condition: |  | New |  | Used |
|  | 2. | Weight of Equipment Empty |  | Lbs |
|  | 3. | Weight of Attachments: |  |  |
|  | a. | Platforms and Ladders |  | Lbs |
|  | b. | Piping and Accessories |  | Lbs |
|  | c. | Liquids Inside |  | Lbs |
|  | d. | Dirt and Debris |  | Lbs |
|  | e. | Internal Trays or Liners |  | Lbs |
|  | 4. | Total Weight of Equipment |  | Lbs |
| B. | Total Load |  |  |
|  | Erection Crane |
| 1. | Percent of Equipment Weight |  | % | 7. | Weight of Jib Erected |  | Lbs. |
| 2. | Amount of Eqiupment Weight |  | Lbs. |  | Stored |  | Lbs. |
| 3. | Weight of Headache Ball |  | Lbs. | 8. | Weight of Jib Headache Ball |  | Lbs. |
| 4. | Weight of Block |  | Lbs. | 9. | Weight of Cable (Load Fall) |  | Lbs. |
| 5. | Weight of Lifting Bar |  | Lbs. | 10. | Auxiliary Boom Head |  | Lbs. |
| 6. | Weight of Slings and Shackles |  | Lbs. | 11. | Other: __________________ |  | Lbs. |
|  | Total Weight |  | Lbs. |  |  |
|  | Tailing Crane |
| 1. | Percent of Equipment Weight |  | % | 7. | Weight of Jib Erected |  | Lbs. |
| 2. | Amount of Eqiupment Weight |  | Lbs. |  | Stored |  | Lbs. |
| 3. | Weight of Headache Ball |  | Lbs. | 8. | Weight of Jib Headache Ball |  | Lbs. |
| 4. | Weight of Block |  | Lbs. | 9. | Weight of Cable (Load Fall) |  | Lbs. |
| 5. | Weight of Lifting Bar |  | Lbs. | 10. | Auxiliary Boom Head |  | Lbs. |
| 6. | Weight of Slings and Shackles |  | Lbs. | 11. | Other: __________________ |  | Lbs. |
|  | Total Weight |  | Lbs. |  |  |
| Source of Load Weight: |  |
| (Name Plate, Drawings, Calculated, Weighed) |
| Weights Verified By: |  |

| C. | Capacities of the Crane |  |  |
| --- | --- | --- | --- |
|  | Erection Crane Configuration |  |  |
| 1. | Type of Crane |  |
| 2. | Rated Capacity |  | Tons |
| 3. | Lifting Arrangement |  |  |
| a. | Max. Radius During Lift |  | Ft. |
| b. | Length of Boom |  | Ft. |
| c. | Angle of Boom at Pick |  | Degree |
| d. | Angle of Boom at Set |  | Degree |
| e. | Rated Capacity Under Most Severe Conditions |  |  |
| 1. | Over Rear |  | Lbs. |
| 2. | Over Front |  | Lbs. |
| 3. | Over Side |  | Lbs. |
| f. | Rated Capacity for Lift |  | Lbs. |
| 4. | Jib |  |  |
| a. | Is the Jib to be used? |  | Yes/No |
| b. | Length of Jib |  | Ft. |
| c. | Jib Angle |  | Deg. |
| d. | Rated Jib Capacity |  | Lbs |
| 5. | Cable |  |  |
| a. | Number of Parts |  |  |
| b. | Size of Cable |  | Inch. |
| c. | Maximum Capacity |  | Lbs |
| D. | Percent of Cranes Capacity |  |  |
|  |  | Total Weight x 100 | = |  | % |
|  |  | Rated Capacity |  |  |  |
| E. | Size of Slings |  |  |
| 1. | Sling Selection |  |  |
| a. | Type of Arrangement |  |  |
| b. | Number of Slings to Hook |  |  |
| c. | Sling Size |  | Inch. |
| d. | Sling Length |  | Ft. |
| e. | Rated Capacity |  | Lbs. |

| C. | Capacities of the Crane |  |  |
| --- | --- | --- | --- |
|  | Tailing Crane Configuration |  |  |
| 1. | Type of Crane |  |
| 2. | Rated Capacity |  | Tons |
| 3. | Lifting Arrangement |  |  |
| a. | Max. Radius During Lift |  | Ft. |
| b. | Length of Boom |  | Ft. |
| c. | Angle of Boom at Pick |  | Degree |
| d. | Angle of Boom at Set |  | Degree |
| e. | Rated Capacity Under Most Severe Conditions |  |  |
| 1. | Over Rear |  | Lbs. |
| 2. | Over Front |  | Lbs. |
| 3. | Over Side |  | Lbs. |
| f. | Rated Capacity for Lift |  | Lbs. |
| 4. | Jib |  |  |
| a. | Is the Jib to be used? |  | Yes/No |
| b. | Length of Jib |  | Ft. |
| c. | Jib Angle |  | Deg. |
| d. | Rated Jib Capacity |  | Lbs |
| 5. | Cable |  |  |
| a. | Number of Parts |  |  |
| b. | Size of Cable |  | Inch. |
| c. | Maximum Capacity |  | Lbs |
| D. | Percent of Cranes Capacity |  |  |
|  |  | Total Weight x 100 | = |  | % |
|  |  | Rated Capacity |  |  |  |
| E. | Size of Slings |  |  |
| 1. | Sling Selection |  |  |
| a. | Type of Arrangement |  |  |
| b. | Number of Slings to Hook |  |  |
| c. | Sling Size |  | Inch. |
| d. | Sling Length |  | Ft. |
| e. | Rated Capacity |  | Lbs. |